## Slide 1: Peer Host List and Multicast
FAE – New England
Paul Schmitt
Notes: Title should be in “Title Case.” Subtitle should be in “ALL CAPS.” Job title should be in “ALL CAPS” as well.

## Slide 2: Setting Discovery Peers List
Four ways, in increasing order of Precedence (ref users manual 14.2)
  Environmental Variable – NDDS_DISCOVERY_PEERS
      Leaving NDDS_DISCOVERY_PEERS undefined defaults Discovery MC receive address to 239.255.0.1 and SHMEM (loopback)
      Defining NDDS_DISCOVERY_PEERS with no MC clears MC receive list (Not the MC send default)
  File NDDS_DISCOVERY_PEERS
    Same notes as Env Variable NDDS_DISCOVERY_PEERS
    Setting NDD_DISCOVERY_PEERS in a file causes Env Variables to be ignored
  XML – Overrides Env variable
    Overrides NDDS_DISCOVERY_PEERS File and Env settings
  Programmatically
    Overrides all settings from above
Notes: First make sure that all QoS (is clear of Discovery peers) – NDDS_DISCOVERY_PEERS file set to .bak, XML in publisher and User shapes QOS is clear and code that sets QoS in publisher is commented out
ENV Variables:
  Example set up in ~/DDSexample/ShapesFullyCompiled, use publisher and Shapes Demo with just USER_RTI_SHAPES_DEMO_QOS.xml
  In one terminal Turn off all setting of NDDS_DISCOVERY_PEERs, reset ENV var by setting (export NDDS_DISCOVERY_PEERS=1.2.3.4 // some bogus address (clears NDDS default discovery peers)
  In another terminal Leave NDDS_DISCOVERY_PEERS blank (unset NDDS_DISCOVERY_PEERS)
  Launch two ShapesDemo Gui’s
  From the terminal with NDDS_DISCOVERY_PEERS=1.2.3.4 launch another ShapesDemo GUI ($NDDSHOME/bin/rtishapesdemo&)
  Start a Shapes ./objs/x…/ShapesType_publiser from each terminal one at a time – first from the (unset NDDS_DISCOVERY_PEERS),
  All three shapes demo GUIs should show the Square Instance
  Kill that publisher and start a pub from the NDDS_DISCOVERY_PEERS=1.2.3.4 terminal
  The two shapes demo GUI launched from the launcher should move, the Shapes DemoGUI launched from the Terminal NDDS_DISCOVERY_PEERS=1.2.3.4 should not move
File
  cp .bak file to NDDS_DISCOVERY_PEERS

## Slide 3: Demo – Env Variable behavior
All sources of Initial Discovery Clear
Set Env var in Left Terminal Window (LTW) to non-existent Host Address
  Clears Just the Discovery Receive MC address – Discovery Send MC address still default 239.255.0.1
unset Env var in Right Terminal Window (RTW)
  Defaults Discovery MC to both send and receive on 239.255.0.1
Start Left and Right Shapes a demo (LSD, RSD) from each LTW and RTW
  LTW and LSD Discovery will not listen but only send on MC 239.255.0.1
  RTW and RSD Discovery will listen and send on MC 239.255.0.1
Result
  Publishing from LTW to LSD – No Discovery: neither the LTW or the LSD are listening for Discovery on a ‘legitimate’ IP or MC address.
  Publishing form LTW to RSD – Asymmetric Discovery: LTW is sending Discovery on 239.255.0.1 but not listening, RSD is sending and listening for discovery on 239.255.0.1 (LTW Send -> RSD Receive Discovery MC 239.255.0.1)
  Publishing from RTW to LSD – Asymmetric Discovery: RTW sending and Listening for discovery on MC 239.255.0.1, LSD is sending Discovery on 239.255.0.1 but not listening (LSD Send -> RTW Receive Discovery MC 239.255.0.1)
  Publishing from RTW to RSD – Symmetric Discovery: RTW and RSD both sending and listening for Discovery on 239.255.0.1

## Slide 4: Demo – NDDS_DISCOVERY_PEERS File Empty
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
The file is empty and will override the Env settings
  LTW and RTW Env vars are overridden by the file and MC Discovery Receive address now set to 239.255.0.1–both will be sending Discovery on MC 239.255.0.1 neither will be listening for Discovery on MC 239.255.0.1
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from LTW to LSD – No Discovery: neither the LTW or the LSD are listening Discovery on a ‘legitimate’ IP or MC address.
  Publishing form LTW to RSD – Asymmetric Discovery: , LTW is sending Discovery on 239.255.0.1 but not listening RSD is sending and listening for discovery on 239.255.0.1 (LTW Send -> RSD Receive Discovery MC 239.255.0.1)
  Publishing from RTW to LSD – No Discovery : neither the RTW or the LSD are listening Discovery on a ‘legitimate’ IP or MC address.
  Publishing from RTW to RSD – Asymmetric Discovery: RTW sending but not Listening for Discovery on MC 239.255.0.1 and RSD both sending and listening for Discovery on 239.255.0.1 (RTW send -> RSD Receive Discovery MC 239.255.0.1

## Slide 5: Demo – NDDS_DISCOVERY_PEERS File MC 239.255.0.1
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
Uncomment the Host Address in NDDS_DISCOVERY_PEERS file
  LTW and RTW Env vars are overridden by the file and Discovery Receive MC address now set to 239.255.0.1
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from LTW to LSD – Asymmetric Discovery: The LTW is now listening, the LSD is only publishing at start up or periodically so there is a delay depending upon the startup order (LSD (periodically) -> LTW (now listening via Peers file)
  Publishing form LTW to RSD – Asymmetric Discovery: , LTW and RSD sending and listening.
  Publishing from RTW to LSD – Asymmetric Discovery: The RTW is now listening, the LSD is only sending discovery at start up or periodically so there is a delay depending upon the startup order (LSD (periodically) -> RTW (now listening via Peers file)
  Publishing from RTW to RSD – Asymmetric Discovery: RTW and RSD sending and listening
Other – re-comment Discovery MC address and uncomment Discovery Host IP address

## Slide 6: Demo – XML QoS no Valid Discovery IP/MC addresses
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
  Note LTW and RTW are the same so we can just use one or the other from her forward
Uncomment the <initial_peers> in USER_QOS_PROFILES.xml file (Leave NDDS_DISCOVERY_PEERS)
  First set Discovery Initial Peers and MC receive address to bogus values
  LTW and RTW Env vars are overridden by NDDS_DISCOVERY_PEERS file are overridden by the xml file
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from TW to LSD – No Discovery: The TW is listening for discovery on default default MC 239.255.0.1 and sending discovery on bogus addresses . The LSD is only sending discovery at start up or periodically and not on anything the TW is listing on.
  Publishing form TW to RSD – Asymmetric Discovery: The TW is listening for discovery on the loopback and sending discovery to bogus addresses. The RSD is sending discovery on the default MC address. (one would have to disable loopback - a separate xml command.)

## Slide 7: Demo – XML QoS w/ Valid Discovery IP/MC addresses
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
Uncomment the <initial_peers> in USER_QOS_PROFILES.xml file (Leave NDDS_DISCOVERY_PEERS)
  Change Discovery Initial_peers in USER_QOS_PROFILES.xml to valid addresses (default MC, New MC, Host)
  TW Env vars are overridden by NDDS_DISCOVERY_PEERS file are overridden by the xml file
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from TW to LSD – Symmetric Discovery:
  Publishing form TW to RSD – Symmetric Discovery:

## Slide 8: Demo – Programmatic Discovery no Valid IP/MC addresses
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
Uncomment the Code for non-valid initial peers setting (Leave xml that has valid addresses)
  Compile and run the publisher
  TW app Env vars are overridden by NDDS_DISCOVERY_PEERS file and XML are overridden programmatically
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from TW to LSD – No Discovery: The TW is listening for discovery on default default MC 239.255.0.1 and sending discovery on bogus addresses . The LSD is only sending discovery at start up or periodically and not on anything the TW is listing on.
  Publishing form TW to RSD – Asymmetric Discovery: The TW is listening for discovery on the loopback and sending discovery to bogus addresses . The RSD is sending discovery on the default MC address and loopback (one would have to disable loopback - a separate xml command.)

## Slide 9: Demo – Programmatic Discovery Valid IP/MC addresses
Use Prior Left and Right Terminal Windows and RTI Shapes Demos from prior slide
  Reset Shapes Demo Config to clear Participant DB – else after a 0 – 60 sec timeout discovery will occur
Change and compile code for valid (matching) Host and / MC address (Leave xml that has valid addresses)
  Compile and run the publisher
  TW app Env vars are overridden by NDDS_DISCOVERY_PEERS file and XML are overridden programmatically
  LSD and RSD will still be using Env Variables – i.e. LSD will be sending but not be listening for discovery on MC and the Unicast Address is invalid. RSD will be both listening and Sending Discovery on 239.255.0.1
Result
  Publishing from TW to LSD – Symmetric Discovery:
  Publishing form TW to RSD – Symmetric Discovery:

## Slide 10: Multicast Discovery non-default and MC User Data
Use wireshark and two subscribers to show MC user data
Use Shape Demo with Config for USER_RTI_SHAPES_DEMO_QOS_PROFILES.xml
First show non MC case with wireshark (default lib)
  duplicate sequence numbers via localhost
Now turn up 2 Demo’s using MC Library using MC lib
  Show Wireshark has only one sequence via MC
Now turn up Shapes_subscriber.o from ~/DDSexamples/ShapesFullyCompiled

## Slide 11: Detect Graceful vs. Liveliness miss participant exit
Settings (use XML and program Shapes_subscriber.o)
  Publish Triangle via ShapeDemo (Use default)
  Set Liveliness to .5 seconds
Run Shapes_subscriber.o from a window and watch receive output, and delete triangle
  message should show that the ’Data instance was disposed’
Now run and then CTRL^C Shapes_publisher.o and note output on Shapes_subscriber.o
  message should now show that the ’’Data Instance no longer has any DataWriter writing it”